## Slide 1: Robotics and human-machine interface
Project report

## Slide 2: Robot creation
The robot is a 7-DOF arm
The robot has 3 revolute joints and 2 spherical joints
The links are defined utilizing the Denavit-Hartenberg convention

## Slide 3: Robot description
d | a | α | ϑ
30 | 0 | π/2 | q1
0 | 50 | 0 | q2
0 | 0 | π/2 | q3
0 | 70 | π/2 | q4
0 | 0 | π/2 | q5
0 | 50 | π/2 | q6
0 | 0 | 0 | q7
All the joints are limited between -π/2 and π/2

## Slide 4: Trajectory planning
Set the trajectory vertices
Obtain the trajectory in the cartesian space utilising the ctraj() function

## Slide 5: Arm movement
For each step of the arm trajectory:
  Compare the transformation matrices of the previous and current step
  Compute the difference in terms of position and rotation angles (ypr)
  Handle the case of angle wrap

## Slide 6: Arm movement
  Compute the required velocity and angle variation rate
  Compute the angular velocity vector from the ypr angles variation rate
  Find , utilising the pseudo-inverse of the geometrical Jacobian matrix

## Slide 7: Arm movement
  Compute , optimising its value according to a specified objective function
  Update the current joints’ position
  where P is a projector in the null space of J

## Slide 8: Manipulability optimization
  The value of can be computed in order to optimize the value of manipulability in every point of the trajectory

## Slide 9: Distance from limits optimization
  The value of can be computed to maximize the distance from the joints’ physical limit in every point of the trajectory

## Slide 10: Distance from limits optimization
  The value of can be computed to maximize the distance of a joint from a specific point in space

## Slide 11: Joint positions plots
The joints coordinates’ evolution during time can be visualized

## Slide 12: Robot animation
The animation can be visualized also with the manipulability ellipsoid